## Slide 1: 01:198:211 Computer Architecture
Abhishek Bhattacharjee
Rutgers University
abhib@cs.rutgers.edu
Spring 2014

## Slide 2: Instructors
Me: Abhishek Bhattacharjee
      abhib@cs.rutgers.edu
      Office Hour: M 5:00-6:00PM (CoRE 306)
TA: Md Haque Section: T 8:25-9:20 PM (LSH-B 105) Contact: mdhaque@cs.rutgers.edu Office Hours: TBA, W 11:00-12:00 PM
TA: Brian Poppy Section: Th 3:35-4:30 PM (BE 252) Contact: bpoppy@cs.rutgers.edu Office Hours: TBA
TA: Chaowei Tan Section: Th 5:15 - 6:10 PM (TIL 251) Contact: ct382@cs.rutgers.edu Office Hours: TBA, F 1:00-2:00 PM
TA: Ioannis Manousakis
Section: T 3:35 - 4:30 PM (BE 252) Contact: im159@cs.rutgers.edu Office Hours: TBA

## Slide 3: Course Web
Course information on:
  Sakai: https://sakai.rutgers.edu
    Announcements, course material, assignment hand-in, etc.
    If you are registered, when you login to Sakai using your netid, you should see a tab “CS 211 F11”
      If not, it may be under the “My Active Sites” tab

## Slide 4: Text Books
Required Book:
  Bryant and O’Hallaron. Computer Systems: A Programmer’s Perspective. Prentice Hall.
  Recommended Book: Patterson and Hennessy. Computer Organization and Design: The Hardware/Software Interface. Morgan Kauffman.
  Kernighan and Ritchie. The C Programming Language, 2nd Edition, Prentice Hall, 1988.
    Any good C book should be fine
    A free online C book: http://publications.gbdirect.co.uk/c_book/
      Disclaimer: I know nothing about the quality of this book

## Slide 5: What You Should Know
Prerequisite: 198:112 
  You know some math
  You know a bit about algorithms
  You know at least one programming language (Java)
  You know something about how to write, run, and test programs

## Slide 6: What You Will Learn …
How to program in two more programming languages (C and Assembly)
The major hardware components in computer systems
  Trends in technology and computer architecture
How hardware components are built from digital logic
How programs written in a high-level language (e.g., C) is actually executed by the hardware
How to understand and improve the performance of programs

## Slide 7: Course Expectations
The fun part
  3 programming assignments
  1 paper & pencil homework assignment
The not so fun part
  2 midterm and 1 final exams
    All exams are comprehensive (all materials up to the exam)
What we expect from you
  Attend lectures and recitations
    Read the assigned readings before lecture
    Read and think about the programming and homework assignments
  Ask questions
  Start programming assignments early

## Slide 8: No Late Assignments
We will NOT accept late assignments
Programming assignments to be handed-in on Sakai
  Deadline will be enforced by Sakai
    Assignments will not be accepted after deadline passes
    Can hand-in assignments multiple times so if you are working at the last minute, hand-in a version early (e.g., ½ hour before deadline)
Homework assignments to be handed-in in lecture
  I will stop accepting assignments once I leave the lecture room
Emails with assignments attached will be discarded

## Slide 9: Collaboration vs. Cheating
Collaboration is encouraged
  You learn by discussing with others
  BUT, must not cheat…
Cheating
  We hate it, we will not tolerate it, we will look for it
  If we find cheating, everyone involved will be punished
    Department’s academic integrity policy: http://www.cs.rutgers.edu/policies/academicintegrity/
  If you are having trouble with the course for any reason
    Come talk to me
      Please observe my “door policy”
    I will help you if I can
      Corollary: once cheating has occurred, there’s nothing I can do to help you avoid the consequences

## Slide 10: Tentative List of Topics
Introduction
  Hardware trends
C programming
Information representation
Assembly (x86) programming
Digital logic
Processor architecture
  Pipelining (?)
Memory hierarchy
Compiling & linking (?)
Measuring & optimizing program performance

## Slide 11: Programming Assignments
3 programming assignments
Program in C and/or Assembly
  Don’t wait until the last minute
  Learn how to use tools
    Don’t program/debug “by accident” or “by blind search”
Will be done using the Instructional Lab
  http://ilab.rutgers.edu
    If you don’t already have an account, get one asap
      http://www.cs.rutgers.edu/resources/new_users/getting_started.whtml
  You will be programming in a Linux environment
    http://www.cs.rutgers.edu/resources/new_users/beginners_doc.whtml
    You can use Eclipse and/or the gnu tools (gcc, gmake, gdb, etc.)
      We’ll point you to documentation on the class Web

## Slide 12: Grading
Grading:
  30%: 2 midterm exams
  30%: final exam (cumulative)
  10%: homework assignments
  30%: programming assignments
No make-up exams except for university sanctioned reasons.
  Must inform professor before the exam
  Informing professor ≠ ok to take make-up

## Slide 13: Computer Architecture
?

## Slide 14: Main Components
CPU
Memory
Bus
I/O devices
  Human Interface
    Mouse, keyboard, screen, etc.
  Storage
  Networking
  Graphics
CPU
Memory
Output
Input
Bus

## Slide 15: Von Neumann Model
0
1
2
Memory
3
4
5
7
6
8
9
Store both
instructions
and data
+
-
*
/
CPU
N
ALU
PC

## Slide 16: Basic CPU Function
FETCH[PC++]
DECODE
EXECUTE
Arithmetic: +, -, *, /
Logic: bre, jmp

## Slide 17: Programming Meets Hardware
High-Level Language Program
Assembly Language Program
Machine Language Program
movl $1, -8(%ebp)
movl $2, -12(%ebp)
movl -8(%ebp), %eax
movl %eax, -16(%ebp)
movl -12(%ebp), %eax
movl %eax, -8(%ebp)
movl -16(%ebp), %eax
movl %eax, -12(%ebp)
movl -16(%ebp), %eax
movl %eax, 12(%esp)
movl -12(%ebp), %eax
movl %eax, 8(%esp)
movl -8(%ebp), %eax
movl %eax, 4(%esp)
7f 45 4c 46 01 01 01
00 00 00 00 00 00 00
00 00 02 00 03 00 01
00 00 00 f0 82 04 08
34 00 00 00 c4 0c 00
00 00 00 00 00 34 00
#include <stdio.h>
int main() {
int x, y, temp;
x=1; y=2;
temp =x; x=y; y=temp;
printf("%d %d %d\n",x,y,temp);
}
ISA
Compiler
Assembler

## Slide 18: Input/Output
0
1
2
Memory
3
4
5
7
6
8
9
+
-
*
/
CPU
N
Devices:
Input: mouse, keyboard
Output: screen, speaker
Storage: disk, tape
Graphics
Networking

## Slide 19: Von Neumann in Practice
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
Expansion slots for
other devices such
as network adapters
PC
Input
Output

## Slide 20: Where Is the OS?
Hardware
OS
App
App
Does this mean apps run
on OS rather than the hardware?
Hardware
OS
App
Apps typically runs directly on
hardware. Will switch over to
OS when need help.
Actually, 1st picture is used frequently because OS does extend the hardware, making the hardware appear more “powerful” through abstractions such as processes, threads, virtual memory, files, etc.

## Slide 21: Computer Architecture
How to design and build the components
How to design and build systems from the components
In this class:
    Understand basics of current components and systems
    Understand how programs run on current systems
    Understand how current architecture affect my high-level language programs
      How can I make my program run faster?
      How can I make my program more power efficient?
        Run longer when on battery

## Slide 22: Architecture Trends: Moore’s law
Gordon Moore was an Intel Engineer
An observation about improvements in hardware
No of transistors on a chip double every 18 months
Exponential growth seen in other hardware dimensions
  Processor speed: 2x every 18 months
  Memory capacity: 2x every 2 years
  Disk capacity: 2x every year

## Slide 23: Number of Transistors on a Chip

## Slide 24: Clock speed

## Slide 25: Processor Performance
    2x every 18 months

## Slide 26: Memory Capacity

## Slide 27: Disk Capacity

## Slide 28: CPU/Memory Performance Gap
Implication: memory hierarchy
  registers, caches
DRAM
7%/yr.
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Processor-Memory
Performance Gap: (grows 50% / year)
Performance
µProc
60%/yr.

## Slide 29: Processor Speed vs. Memory Bandwidth
Source:
Heath, Kaur,
Martin, Nguyen.
HPCA 2001.

## Slide 30: “Power Wall”