## Slide 1: 211: Computer Architecture Spring 2014
Abhishek Bhattacharjee
Topic:
  Data representation

## Slide 2: C Review

## Slide 3: Bug - # 1
scanf(“%d”, val);

## Slide 4: Bug - # 2
Reading Uninitialized Memory
  Assuming that heap data is initialized to zero
/* return y = Ax */
int *matvec(int **A, int *x) {
int *y = malloc(N*sizeof(int));
int i, j;
for (i=0; i<N; i++)
for (j=0; j<N; j++)
y[i] += A[i][j]*x[j];
return y;
}

## Slide 5: Bug - # 3
Overwriting Memory
  Allocating the (possibly) wrong sized object
int **p;
p = malloc(N*sizeof(int));
for (i=0; i<N; i++) {
p[i] = malloc(M*sizeof(int));
}

## Slide 6: Bug - # 4
Overwriting Memory
  Off-by-one error
int **p;
p = malloc(N*sizeof(int *));
for (i=0; i<=N; i++) {
p[i] = malloc(M*sizeof(int));
}

## Slide 7: Bug - # 5
Overwriting Memory
  Misunderstanding pointer arithmetic
int *search(int *p, int val) {
while (*p && *p != val)
p += sizeof(int);
return p;
}

## Slide 8: Bug - # 6
Referencing Nonexistent Variables
  Forgetting that local variables disappear when a function returns
int *foo () {
int val;
return &val;
}

## Slide 9: Bug - # 7
Freeing Blocks Multiple Times
x = malloc(N*sizeof(int));
<manipulate x>
free(x);
y = malloc(M*sizeof(int));
<manipulate y>
free(x);

## Slide 10: Bug - # 8
Referencing Freed Blocks
x = malloc(N*sizeof(int));
<manipulate x>
free(x);
...
y = malloc(M*sizeof(int));
for (i=0; i<M; i++)
y[i] = x[i]++;

## Slide 11: Bug - # 9
Failing to Free Blocks (Memory Leaks)
  Slow, long-term killer
foo() {
int *x = malloc(N*sizeof(int));
...
return;
}

## Slide 12: Bug - # 10
Failing to Free Blocks (Memory Leaks)
  Freeing only part of a data structure
struct list { int val; struct list *next;};
foo() {
struct list *head =
malloc(sizeof(struct list));
head->val = 0;
head->next = NULL;
<create and manipulate the rest of the list>
...
free(head);
return;
}

## Slide 13: What Do Computer Do?
Manipulate stored information
Information is data
  How is it represented?
Basic information: numbers
Human beings have represented numbers throughout history
  Egyptian number system
  Roman numeral
Typically decimal
  Natural for humans
Discoveregypt.com

## Slide 14: Number System
Comprises of
  Set of numbers or elements
  Operations on them
  Rules that define properties of operations
Need to assign value to numbers
Let us take decimal
  Base 10
  Numbers are written as dn...d2d1d0
  Each digit is in [0-9]
  Value of a number is interpreted as

## Slide 15: Binary Numbers
Base 2  each digit is 0 or 1
Numbers are written as dn...d2d1d0
Value of number is computed as
Binary representation is used in computers
  Easy to represent by switches (on/off)
  Manipulation by digital logic in hardware
Written form is long and inconvenient to deal with

## Slide 16: Hexadecimal Numbers
Base 16
Each digit can be one of 16 different values
  Symbols = {0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F}
First 10 symbols (0 through 9) are same as decimal
  A=10,B=11,C=12, D=13, E=14, F=15
Numbers are written as dn...d2d1d0
Value =

## Slide 17: Octal Numbers
Base 8  each digit is in [0-7]
Numbers are written as dn...d2d1d0
Value of number is computed as

## Slide 18: Converting Hex to Binary
Each hexadecimal digit can be represented by 4 binary digits
  Why?
0x2A8C (hex) = 0b0010101010001100 (binary)
  0xC = 12 x 160 = 8 + 4 = (1 x 23) + (1 x 22) = 0b1100
  0x80 = 8 x 161 = 23 x 24 = 27 = 0b 10000000
  And so on …
So, to convert hex to binary, just convert each digit and concatenate
What about octal to binary?

## Slide 19: Converting Binary to Hex
Do the reverse
  Group each set of 4 digits and change to corresponding digit in hex
  Go from right to left
Example 1011011110011100
  0b1011011110011100 = 0xB79C
What about binary to octal?

## Slide 20: Decimal to Binary
What’s the largest p, q, r … such that
  n = 2p + r1, where r1 < 2p
  n - 2p = 2q + r2, where r2 < 2q
  n – (2p + 2q)= 2r + r3, where r3 < 2r
  …
The above means that
  n = (1 x 2p) + (1 x 2q) + (1 x 2r) + … + rm , where rm = n % 2
  Can you see why this now allows n to be easily written in binary form?
Example: convert 21 to binary
  21 = 24 + 5, 5 = 22 + 1 21 = 0b10101

## Slide 21: Decimal to Binary and Back
How to do the conversion algorithmically?
What about binary to decimal?
What about decimal to hex? Hex to decimal?
Decimal to octal? Octal to decimal?
Hex to octal? Octal to Hex?

## Slide 22: Decimal and Binary fractions
In decimal, digits to the right of radix point have value 1/10i for each digit in the ith place
  0.25 is 2/10 + 5/100
Similarly, in binary, digits to the right of radix point have value 1/2i for each ith place
  Just the base is different
8.625 is 1000.101
  .625 = 6/10 + 2/100 + 5/1000 = 1/2 + 1/8
How to convert?

## Slide 23: Decimal to Binary Example
Example: 0.625 to binary
  ANS: 0.101
    0.625*2 = 1.25
    output 1
    0.25*2 =0.5
    output 0
    0.5*2 = 1
    output 1
    Exit
Algorithm
Number = decimalFraction
while (number > 0) {
number = number*2
if (number >=1) {
Output 1;
number = number-1
}
else {
Output 0
}
}
Why does it work?

## Slide 24: Data sizes
All Information is represented in binary form but require different sizes
Characters in 1 byte, integers 2 to 4 bytes, real numbers 4 to 8 bytes
C declaration | 32-bit machine | 64-bit machine
char | 1 | 1
short int | 2 | 2
int | 4 | 4
pointer | 4 | 8
float | 4 | 4
double | 8 | 8

## Slide 25: Big Endian vs. Little Endian
How to determine value when have a binary number spread across multiple bytes
Is it A0BC0012 or 1200BCA0?
  One is called “big endian” and one is “little endian”
    Most Significant byte first … big endian
    Lease significant byte first … little endian
  Makes no difference to computer architecture
Why do we care?
  Interpret machine code and values
  One computer (big endian) sending data to another computer (little endian)
  Need to convert into standard form before transmitting
A0 BC 00 12

## Slide 26: Representing integers
How do we represent negative numbers in computers?
  Use a bit … after all, that’s how we store information, right?
Signed Magnitude:
  0100 = 4, 1100 = -4
  0011 = 3, 1011 = -3
What is 1000?
  Have two zeros +0 (0000) and -0 (1000)
  As we shall see, inconvenient for arithmetic computations
S
Magnitude

## Slide 27: One’s Complement
Represent negative numbers by complementing positive numbers
Still have two zeros but arithmetic computation becomes easier
000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
0 | 1 | 2 | 3 | -3 | -2 | -1 | -0

## Slide 28: Two’s Complement
000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
0 | 1 | 2 | 3 | -4 | -3 | -2 | -1
One’s complement plus one
  Most significant bit still gives the “sign”
  Trick: copy all ‘0’ bits from LSB till first ‘1’ bit. Copy ‘1’ bit, then flip all remaining bits till MSB.
Advantages:
  Only 1 zero
  Most convenient for arithmetic computations
Used in almost all computers today

## Slide 29: Numerical Value of Two’s Complement
Given a two’s complement number of length n, written as dn-1…d1d0
  It’s value is interpreted as
The range of values is then
  More negative numbers than positive (if we do not count 0)
  101 = ?
  0101 != 101

## Slide 30: ASCII
A character is stored as 1 byte according to the ASCII standard
Originally used only 128 values (7 bits)
  One bit could be used for error detection (will discuss later)
Subsequently extended to use all 256 values

## Slide 31: ASCII table

## Slide 32: Unicode and UTF-8
What about characters for other languages?
Unicode is a standard that defines more than 107,000 characters across 90 scripts (and more …)
Unicode can be implemented by different character encodings
Most common: UTF-8
  Variable length encoding of Unicode: 1-4 bytes for each character
  1-byte form is reserved for ASCII for backward compatibility

## Slide 33: Floating point
Integers typically written in ordinary decimal form
  E.g., 1, 10, 100, 1000, 10000, 12456897, etc.
But, can also be written in scientific notation
  E.g., 1x104, 1.2456897x107
What about binary numbers?
  Works the same way
  0b100 = 0b1x22
Scientific notation gives a natural way for thinking about floating point numbers
  0.25 = 2.5x10-1 = 0b1x2-2
How to represent in computers?

## Slide 34: IEEE floating point standard
Most computers follow IEEE 754 standard
Single precision (32 bits)
Double precision (64 bits)
Extended precision (80 bits)
S
Fraction
Exponent

## Slide 35: Floating point in C
32 bits single precision (type float)
  1 bit for sign, 8 bits for exponent, 23 bits for mantissa
    Sign bit: 1 = negative numbers, 0 = positive numbers
    Exponent is power of 2
  Have 2 zero’s
  Range is approximately -1038 to 1038
64 bits double precision (type double)
  1 bit for sign, 11 bits for exponent, 52 bits for mantissa
  Majority of new bits for mantissa  higher precision
  Range is -10308 to +10308

## Slide 36: Numerical Values
Three different cases:
  Normalized values
    exponent field ≠ 0 and exponent field ≠ 2k-1 (all 1’s)
    exponent = binary value – Bias
      Bias = 2k-1-1 (e.g., 127 for float)
    mantissa = 1.(mantissa field)
    Ex: (sign: 0, exp: 1, mantissa: 1) would give 0b1.1x2-126
  Denormalized values
    exponent field = 0
    exponent = 1 – Bias (e.g., -126 for float)
    Mantissa = mantissa field (no leading 1)
    Ex: (sign: 0, exp: 0, mantissa: 10) would give 0b10x2-126
  Special values: represent +∞, -∞, and NaN

## Slide 37: Decimal to IEEE Floating Point
5.625
In binary
101.101  1.01101 x 22
Exponent field has value 2
  add 127 to get 129
Exponent is 10000001
Mantissa is 01101
Sign bit is 0
0 10000001 0110100000000000000000

## Slide 38: One more example
Convert 12.375 to floating point representation
Binary is 1100.011
1.100011 x 23
Exponent = 127 + 3 = 130 = 0b10000010
Mantissa = 100011
Sign = 0

## Slide 39: Extended precision
80 bits used to represent a real number
1 sign bit, 15 bit exponent, 64 bit mantissa
20 decimal digits of accuracy
10-4932 to 104932
Not supported in C